## Slide 1: A user-Friendly Tool to measure blood flow velocity and blood cells count in zebrafish videos
Software package compiled in Python for research to analyze blood flow velocity and blood cells count in animal model zebrafish dorsal aorta videos
Ali Farhan and Chung-Der Hsiao
Chung Yuan Christian University, Taiwan

## Slide 2: Introduction
Using AI-based OpenCV library to detect automatically blood flow velocity in zebrafish and medaka videos
Optical flow concept used to analyze the blood flow velocity in dorsal aorta of zebrafish and medaka
Results being validated on the basis of comparison with previously published method of this lab as ImageJ

## Slide 3: Setup for automatic blood flow velocity analysis for zebrafish and medaka
2D video recording using high speed CCD
Installation of Python 3.9 or above version
Download essential computer vision packages
Open command prompt window
Access folder and select type of fish video
Open video in Python (mp4 format)
Use the command to run program and press option 0 for zebrafish and 1 for medaka
Use cursor on window opened for video
Automatic ROI will be selected at the location of dorsal aorta in separate window
Press space key to initiate analysis
Results display with oscillation graph patterns
Optical Flow estimation

## Slide 4: Video Recording using HiBestViewer Application (AZ Instrument, Taiwan)
Resolution : Size of the video taken with a linear correlation to sharpness and clarity.
Exposure time camera exposed : duration of time in which the sensor within the to light
Auto Shot Speed : number of frames taken in one second for the recording (fps)
Record Frame : Number of frame set manually by the user to determine the recording length. The final duration of the video is presented in Record Time. This number cannot exceed the Max Frames or 0.
Preview : Start viewing the current condition of the object of interest under the microscope.
Trigger : Start recording
Stop : Stop the recording or the viewing.

## Slide 5: Steps to Initialize program
Put mp4 format video in folder of the system
Download Python 3.9 or above version from(https://www.python.org/downloads/)
Create folder with name as per desired by the user
Place the zebrafish or medaka dorsal aorta videos in the folder and format of the videos must be mp4
Open command prompt window from ‘start’ panel of system
Program does not require GPU it can be processed on average CPU
No need to use anaconda prompt

## Slide 6: Python installation
After downloading the python 3.9 version from the link mentioned in previous slide, user have to extract the .exe file and click install

## Slide 7: Check system’s specifications as 64-bit
Click on add path

## Slide 8: Check features AND THEN INSTALL
Select for all users

## Slide 9: Check the installation in cmd window
Write the command and confirm the installation

## Slide 10: Essential requirements to initialize Openbloodflow package
Have to extract package zip file at desired location of system:

## Slide 11: Necessary modules to install the package
Pip
Package Installer for Python is the de facto and recommended package-management system written in Python and is used to install and manage software packages. It connects to an online repository of public packages, called the Python Package Index.
Pandas
pandas is a software library written for the Python programming language for data manipulation and analysis. In particular, it offers data structures and operations for manipulating numerical tables and time series.

## Slide 12: Install the program libraries using pip command in cmd propmpt window
Python 3.8 and above version required
Following libraries have to install using command prompt in windows:
Pip install pillow
Python3 –m pip install –upgrade pip
Pip install tk
Pip install pyautogui
Pip install opencv-python
Pip install vidstab
Pip install math
Pip install numpy
Pip install matplotlib
Pip install pandas
Pip install regex
Pip install threadpool==1.3.2
Install the libraries using command prompt
Wait for installation time depending on system’s specifications
The successful installation of each module shall display the message in command prompt

## Slide 13: Open .bat file to run gui
By selecting run.bat file GUI will be displayed

## Slide 14: Windows based setup
The tool is designed for easy installation and operation on windows operating system
Graphical User Interface OpenBloodFlow

## Slide 15: Outlooking of GUI
The preview of selected ROI of dorsal aorta was challenging part to set in central window.
In order to grasp the stabilized view of dorsal aorta of masked window by using tkinter module
On click event of ‘Select ROI Automatic’ button and ‘Select ROI Manually’ button is_selected variable is set to True and False respectively.
After setting this variable, paths of all videos got from the folder location selected by user.

## Slide 16: Steps to start analysis
Upload Videos folder
Selecting ROI

## Slide 17: Dorsal Aorta Preview in GUI

## Slide 18: Results Blood flow velocity

## Slide 19: Results saved in graphs folder

## Slide 20: Analyze Blood Cells count
Open same folder where program files are placed and open “Graphs” Folder
Open csv file to get per frame blood cell count

## Slide 21: comparison
In the csv file per frame data of number of cells passing in Region of Interest at time (1 minute) elongated video of (10 seconds) 200fps being presented.
The Graph chart exhibited average of blood cell count data showing in csv file.
2
7
5
6
3
1
4
8
11
9
12
10
13
15
16
14
Comparison shown in figures to validate the blood cells count
Highlighted blood cells
Original blood cells

## Slide 22: Thanks to ai network